## Slide 1
D4-Equivariant CNN
for SAR Avalanche Segmentation
100× fewer parameters. Better instance detection.
Guillermo San Marco · April 2026
Notes: We built a tiny D4-equivariant CNN for avalanche deposit segmentation in bi-temporal
Sentinel-1 SAR. Headline: we tie the published Gatti 2024 Swin-UNet on pixel F1
using about 1% of the parameters, and we show that the standard pixel metric hides a
10.7-point gap on instance-level F1. I'll walk through the architecture, the
experimental journey, the negative results, and the metric finding. ~15 minutes.

## Slide 2
The problem
Sentinel-1 bi-temporal SAR · tiny, arbitrarily-oriented deposits
• Avalanche deposits are small — often <1% of scene pixels
• Only visible as a difference between pre-event / post-event acquisitions
• Orientation w.r.t. the radar frame has no physical meaning
• SAR is noisy — speckle, incidence-angle effects, terrain shadowing
• Public baseline: Gatti 2024 Swin-UNet, pixel F1 ≈ 0.79
D4-Equivariant SAR Avalanche Segmentation
2 / 18
Notes: SAR is noisy and deposits are tiny. The only reliable signal is the difference
between a pre-event and post-event scene. Critically, a deposit's orientation w.r.t.
the radar frame has no physical meaning — the satellite flies a specific track but
the avalanche doesn't know that. Gatti et al. 2024 published a Swin-UNet baseline
at pixel F1 around 0.79 — that's our reference point. The image on the right is a
representative scene pair with the deposit mask overlaid.

## Slide 3
The research question
Published baseline
Swin-UNet (Gatti 2024)
• ~60 M parameters
• Learns rotation invariance from augmentation
• Test pixel F1 ≈ 0.79
Our proposal
D4-equivariant CNN
• Rotation / reflection symmetry baked into the architecture
• How small can we go?
• 8 symmetries: {id, r90, r180, r270, 4× flips}
D4-Equivariant SAR Avalanche Segmentation
3 / 18
Notes: The Swin-UNet has 60 million parameters and learns rotation/reflection invariance
implicitly through augmentation. Our question: if that invariance is a known physical
property of the problem, what happens when we bake it into the architecture instead
of learning it? We use D4 — the dihedral group of order 8, the eight symmetries of
the image square.

## Slide 4
What D4 equivariance buys us
Encoder exactly equivariant · full model approximately equivariant
Input x g · x (rotated/flipped)
│ │
▼ ▼
┌─────────┐ ┌─────────┐
│ Encoder │ │ Encoder │
└─────────┘ └─────────┘
│ │
▼ ▼
Encoder(x) ── g · ─▶ Encoder(g·x) ← EXACT
│ │
▼ ▼
GroupPool GroupPool
│ │
▼ ▼
invariant(x) ─────── = ─▶ invariant(g·x) ← EXACT
│ │
▼ ▼
Conv2d Decoder Conv2d Decoder ← approximate
│ │
▼ ▼
logit(x) ≈ g⁻¹ · logit(g·x) ← approximate
D4-Equivariant SAR Avalanche Segmentation
4 / 18
Notes: Equivariance means: rotate the input, the output rotates the same way — by construction.
Our encoder is exactly equivariant thanks to escnn — verified in CI on every push.
After GroupPooling we have an invariant representation. The decoder is standard
Conv2d, so the full model is only approximately equivariant. This is a deliberate
trade-off: the decoder keeps the parameter count tiny and allows skip connections.

## Slide 5
Architecture
12-channel bi-temporal SAR input (B, 12, H, W)
├── post = [VH, VV, log-ratio, RGD, LIA, ...] idx 0–5
├── pre = [VH, VV, <shared derived 2–5>] idx 6,7,2–5
└── extra = [DEM, slope, ...] idx 8–11
│
▼
┌─────────────────────────────────────────────────────────┐
│ D4-equivariant encoder (escnn, N=4, with flips) │
│ shared weights across pre / post branches │
│ │
│ post ─► enc(post) pre ─► enc(pre) │
│ │ │ │
│ └────── difference ────┘ │
│ │ │
│ GroupPooling ─► invariant tensor │
└─────────────────────────────────────────────────────────┘
│
▼
Conv2d decoder (4 stages, skip from invariant trunk)
│
├── seg head ─► logit (B, 1, H, W)
└── area head ─► area_m² (B, 1)
PARAMS
625,617
~1% of
Swin-UNet
D4-Equivariant SAR Avalanche Segmentation
5 / 18
Notes: Twelve input channels — pre and post SAR plus derived features: log-ratio, incidence
angle, DEM. The encoder is five equivariant blocks with weights shared across pre
and post branches. We take the difference in the regular representation — still
equivariant — then GroupPool to get an invariant tensor. The decoder is plain Conv2d
with skip connections from the invariant trunk. Total parameter count: 625k — about
1% of Swin-UNet. This number is locked by a CI test called test_parameter_count.

## Slide 6
The experimental journey
Every arrow is a SLURM sweep on Hyak
gatti_mirror.sh cond1, no aug, no skip F1 ~0.75
│
▼
aug_experiment.sh aug 1× / 3× / 5× aug3× wins
│
▼
reg_sweep 1/2/3/3b depth, wd, focal-tversky, ... bigger hurts
│ warm restarts hurt
▼
lambda_sweep.sh component-IoU λ grid bimodal trade-off
│
▼
calibration_sweep T-scale / Platt / isotonic marginal gain
│
▼
★ cond1, no-skip, aug3×, seed 1 F1 = 0.7938 ★
D4-Equivariant SAR Avalanche Segmentation
6 / 18
Notes: Every arrow here is a SLURM sweep on Hyak. Started by mirroring Gatti's setup —
no augmentation, no skip — F1 around 0.75. Augmentation sweep: 3x rotation/flip is
optimal. Regularization sweeps said: bigger models hurt, warm restarts hurt, heavy
regularization hurts. That's evidence for the inductive-bias story — we don't need
more capacity. Lambda sweep on component-IoU loss showed a bimodal trade-off — next
slide. Final config: condition 1 loss, no-skip variant, aug 3x, seed 1 — pixel
F1 0.7938.

## Slide 7
Negative result: λ sweep trade-off
Component-IoU loss weight has no single optimum
• Low λ → better pixel F1, fragmented small deposits
• High λ → better small-instance recall, pixel F1 drops
• No single λ wins both axes
• The loss is a dial, not a setting — which end depends on use case
D4-Equivariant SAR Avalanche Segmentation
7 / 18
Notes: We built a component-IoU variant from Kofler et al.'s blob-loss family. The lambda
sweep showed a bimodal trade-off: low lambda favors pixel F1, high lambda favors
detecting small deposits. No single value dominates. Calling this out because the
literature usually reports a single number; we're saying the loss is a dial, not a
setting — which end you want depends on your downstream use case.

## Slide 8
The methodological punchline
Same predictions, same ground truth — different metric, different story
Pixel F1
ours 0.794
Gatti 0.791
Δ = +0.003
a tie.
Instance F1
ours 0.620
Gatti 0.513
Δ = +0.107
a real gap.
D4-Equivariant SAR Avalanche Segmentation
8 / 18
Notes: Here's the finding. On pixel F1 — the standard metric everyone reports — we tie
Gatti. Three thousandths of a point. That's noise. But on instance F1, with a
center-point matching rule, we're ahead by 10.7 percentage points. Same predictions,
same ground truth, different metric, completely different story. This is the core
methodological contribution of the work.

## Slide 9
Metric disagreement — the picture
D4-Equivariant SAR Avalanche Segmentation
9 / 18
Notes: This is the slide to remember. Left bar group: pixel F1 — bars the same height.
Right bar group: instance F1 — clear gap. We're not better at labeling pixels.
We're better at producing one clean prediction per deposit instead of several
fragmented ones.

## Slide 10
Where the gap comes from — D-scale breakdown
EAWS destructive-size classes · larger deposits = operational relevance
D-scale
ours
Gatti
Δ
D1 (small)
0.31
0.27
+0.04
D2
0.58
0.49
+0.09
D3
0.71
0.58
+0.13
D3 is where the gap is largest — and D3 is what practitioners act on.
D4-Equivariant SAR Avalanche Segmentation
10 / 18
Notes: The instance-F1 gap isn't uniform across deposit sizes. Broken down by EAWS D-scale —
the European avalanche standard — the biggest gap is at D3, destructive-size deposits.
13 percentage points. That matters operationally. D3 is what triggers road closures
and rescue dispatch. Our symmetry-aware model produces a single clean D3 deposit
where Gatti's fragments into 3-4 high-confidence blobs.

## Slide 11
Why: fragmentation
Gatti's big deposits split into multiple high-confidence blobs
• Gatti's predictions fragment large deposits
• Pixel F1 doesn't care — pixels still mostly right
• Instance F1 penalizes fragmentation once per deposit
• Equivariant encoder → smoother orientation-invariant features, fewer spurious local peaks
D4-Equivariant SAR Avalanche Segmentation
11 / 18
Notes: Look at the failure-mode panels. Ground truth: one deposit. Gatti's prediction
breaks it into three blobs with gaps. Pixel-wise still mostly right. But counted
as instances, that's false positives plus a missed true positive. Our model produces
one contiguous prediction. The equivariant encoder gives a smoother
orientation-invariant feature map — fewer local spurious peaks.

## Slide 12
Parameter efficiency
Pareto-dominant on params × F1
0.63 M parameters · two orders of magnitude below Swin-UNet · same pixel F1
D4-Equivariant SAR Avalanche Segmentation
12 / 18
Notes: Pareto plot. X-axis: parameter count. Y-axis: pixel F1. Our point sits alone in the
bottom-right — same F1, two orders of magnitude fewer parameters. This matters for:
(1) edge / near-real-time deployment, (2) training data efficiency, (3) environmental
cost of the research workflow itself.

## Slide 13
Calibration
Both models asymmetrically miscalibrated · temperature scaling doesn't change F1 ranking
• Over-confident at high probabilities
• Under-confident at low probabilities
• Temperature scaling helps marginally
• F1 ranking invariant to calibration choice
• Ship with T-scaling on; document the residual asymmetry
D4-Equivariant SAR Avalanche Segmentation
13 / 18
Notes: Quick slide on calibration. Both models over-confident at the high end and
under-confident at the low end. Temperature scaling gives a marginal improvement
but doesn't change the F1 ranking. We ship with T-scaling on and document the
residual asymmetry so downstream users know what they're getting.

## Slide 14
Honest negative results
Bigger models hurt
confirms inductive-bias story, not scale
Heavy regularization hurt
equivariance already regularizes
Warm restarts hurt
loss landscape isn't the blocker
DPR instance head failed
150 crops vs 30k patches → catastrophic forgetting
D4-Equivariant SAR Avalanche Segmentation
14 / 18
Notes: Every one of these cost us a week. Bigger models hurt — evidence for inductive bias
over scale. Heavy regularization hurt — the equivariance already regularizes, don't
pile on. Warm restarts hurt — the loss landscape isn't the blocker. And the DPR
instance-segmentation head never converged: 150 instance crops couldn't compete with
30k pixel patches, and we saw catastrophic forgetting of the pre-trained encoder.
We're calling this out because the community has a bias toward success stories.

## Slide 15
Reproducibility
• CI green — 7 tests on every push
• encoder equivariance (escnn check_equivariance)
• GroupPooling invariance · determinism
• shape + parameter-count locked
• Final checkpoint + eval JSON committed
• norm_stats_12ch.json committed (force-added)
• SLURM scripts env-var templated — no hardcoded cluster paths
tests/test_equivariance.py 7 tests ✓
data/norm_stats_12ch.json committed
results_final/
eval_cond1_seed1_s16_tta.json F1=0.7938
prob_p2_tromso.npy our probs
prob_gatti_tromso.npy baseline probs
gt_tromso.npy GT
vh_tromso.npy VH viz
.env.example ← REPO DATA_DIR SIF BIND_ROOT
D4-Equivariant SAR Avalanche Segmentation
15 / 18
Notes: Repro matters. Seven CI tests on every push — encoder equivariance via escnn's own
check, GroupPooling invariance, determinism, shape, parameter count locked. Final
checkpoint and eval JSON both committed. Norm stats file committed — it was in
.gitignore and I force-added it. SLURM scripts use environment variables so nothing
is hardcoded to my Hyak account. Anyone can reproduce this in a fresh clone.

## Slide 16
File-by-file map
src/models/segnet.py D4SegNet + D4SegNetNoSkip, _eq_block
src/data/ dataset, preprocess, norm_stats, augment
src/losses.py bce / focal_tversky / dice / component_iou / area
src/train.py loop, AMP, val-F1 checkpoint selection
src/inference.py sliding window, 4 blending modes, 4-fold TTA
src/evaluate.py bootstrap CIs, permutation test, F1-opt threshold
src/aggregate.py roll up run JSONs → comparison tables
src/slurm/*.sh 12 parameterised sweep scripts
tests/test_equivariance.py CI sanity (7 tests)
wiki/ living lab notebook (goal, arch, eval, log, ...)
figures/ hero, metric_disagreement, param_frontier, ...
results_final/ final numbers + probs for the Tromsø scene
D4-Equivariant SAR Avalanche Segmentation
16 / 18
Notes: Quick tour. Model lives in segnet.py. Data handling has its own subpackage.
Losses are modular — pick one with a flag. train.py does the loop with AMP and
F1-based checkpointing. inference.py handles sliding-window with four blending
modes and 4-fold TTA. evaluate.py does bootstrap confidence intervals and
permutation tests against the baseline. SLURM scripts are env-var templated.
The wiki is a living lab notebook — if you want to know why we made a decision,
it's there, dated.

## Slide 17
Take-homes
1
Symmetry-aware inductive bias beats scale
at 1% the parameters, same pixel F1, better instance F1
2
Pixel F1 hides fragmentation
the metric you report is a scientific choice, not a formatting choice
3
Don't ship instance heads without instance data
DPR failed on 150 crops — data scarcity beats architectural cleverness
D4-Equivariant SAR Avalanche Segmentation
17 / 18
Notes: Three take-homes. One: for a problem with known symmetry, encoding it beats learning
it — at a hundredth of the parameters. Two: the metric you report is a scientific
choice, not a formatting choice. Pixel F1 was structurally blind to the fragmentation
gap. Three: the DPR negative result says data scarcity beats architectural cleverness
every time. If you're about to add an instance head, count your instance labels first.

## Slide 18
Thanks.
Questions?
github.com/gsanmarco/Equivariant-SAR-Segmentation
CI green · Checkpoint released · Figures in /figures · Wiki in /wiki
Notes: Happy to go deeper on: escnn group representation details, the instance-matching
rule (center-point with IoU tie-break), copy-paste augmentation ablation, or the
DPR catastrophic-forgetting analysis. All numbers are bootstrap CIs plus permutation
tested — nothing is cherry-picked.